## Slide 1: Virtual Wind Tunnel
Luke Blades, Heather Bolt, Felix Browne, Edward Crinion, David Docherty, Luke Hamilton, Dan Nima, James Walton

## Slide 2: Introduction
Aim
Investigate the integration of Computer Aided Design (CAD), Computational Fluid Dynamics (CFD) and experimentation in automotive design
Deliverables
Design and manufacture concept car model
Create virtual wind tunnel in which to test the CAD model
Rebuild wind tunnel test section and use to validate simulations
Sub-Group Structure
Design
Experimental
High Performance Computing (HPC)

## Slide 3: Design Sub-Group
  Concept car design
  Production of scale models using Additive Layer Manufacture (ALM)
  Investigation of suitable meshing strategies
  Virtual rendering of final concept car design

## Slide 4: Design: Concept Car
Concept car design evolution
RANS CFD analysis

## Slide 5: Design: ALM of Scale Models
Material jetting process used to produce scale models

## Slide 6: Design: Mesh Generation Overview
Critical step in CFD process
Affected by many factors
Mesh quality can be measured in various ways
Multiple methods for improving quality, post-assessment

## Slide 7: Design: Mesh Experimentation Results
Solution accuracy comparison for various meshing schemes
Mesh quality information collected
Tet PI found to be most robust and accurate: variance of 3.73% from experimental
Tet PI then used on final concept car later on
Chart: No. Elements
| 23161 | 192231 | 267018 | 574786 | 1003046 | 1613160 | 2120754 | 2552671 | 3961136
Tet's (PD) | 0.66319 | 0.46227 | 0.44666 | 0.38079 | 0.35769 | 0.33169 | 0.32395 | 0.32088 | 0.31515
Hybrid | 0.66319 | 0.51166 | 0.46692 | 0.38809 | 0.36171 | 0.33115 | 0.32431 | 0.31846 | 0.31337
Cut-Cell | 0.65535 | 0.55413 | 0.53769 | 0.2875 | 0.3016 | 0.29081 | 0.27984 | 0.27481 | 0.26828
Tet's (PI) | 0.46586 | 0.5557 | 0.50416 | 0.37486 | 0.35138 | 0.32287 | 0.32306 | 0.31828 | 0.31015
Experimental | 0.299 | 0.299 | 0.299 | 0.299 | 0.299 | 0.299 | 0.299 | 0.299 | 0.299

## Slide 8: Design: Rendering
Aim: render the concept car in Exeter
Used path-tracing light solving method in Blender
Data from Electronic Distance Measuring (EDM) and Google Earth
Photons from each pixel are traced back

## Slide 9: Design: Rendering
Blender is partially written in Python, so a script can automate the process
‘Drivers’ link different objects’ parameters
Wheel rotation is dependent on car displacement, for example

## Slide 10: Design: Rendering
At this complexity, rendering takes 15 minutes per frame

## Slide 11: Design: Rendering

## Slide 12: Design Group Summary
Iteratively designed concept car
Delivered physical model for testing
Delivered CAD model for virtual testing
PI Tet found to be the most robust and accurate meshing process
Rendered model in virtual environment

## Slide 13: Experimental Sub-Group
Responsible for gathering real wind tunnel data for the concept car, comparable to CFD results
Drag forces were obtained through the use of drag balances and a wake survey
A wind tunnel was modified to provide this data

## Slide 14: Experimental: Test Section Rebuild
The test section of an open return wind tunnel was redesigned and rebuilt
This improved model visibility for smoke visualisation through fully transparent top and front
It also supported the use of automated wake survey equipment

## Slide 15: Experimental: Automated Probe Positioning
To perform the wake survey a probe (either pitot-static tube or hot wire anemometer) had to be positioned automatically
This system was powered with stepper motors and controlled with a Raspberry Pi computer, on which a python script was written

## Slide 16: Experimental: Wake Survey
Two – dimensional wake surveys were obtained using the probe positioning system
This provided a square grid of velocity measurements taken 5mm apart
From these, Von Karman's principle of momentum conservation was used to calculate the total drag on the car by summing the momentum losses

## Slide 17: Experimental: Drag Balance
The second experimental method involved using a drag balance

## Slide 18: Experimental: Drag Balance
S-Beam Load Cell: ±0.005N
Digital Force Meter: ±0.049N

## Slide 19: Experimental: Angle of Cable
In this case:
  x = 290mm
  y = 1.99mm
  Therefore, from trigonometry, θ = 0.39⁰

## Slide 20: Summary of Experimentation
Redesigned and built a new wind tunnel test section
Concept Car Drag Coefficients:
  Wake Survey (Angled): 0.358 ± 0.077
  Drag Balance (Straight): 0.17± 0.015

## Slide 21: HPC Sub-Group
OpenFOAM used due to it being open-source, this allowed for parallel processing on many cores
Responsible for gathering computational results for the concept car, to be verified by the experimental team
Considered a variety of turbulence models and meshing methods to create the final virtual wind tunnel case setup
Explored the influence of urban canyon flow on the aerodynamic properties of a vehicle
Investigated a surrogate-based modelling approach

## Slide 22: HPC: Environment Creation
Using an Electronic Distance Measuring (EDM) Total Station, the area was mapped out
Co-ordinate data manipulated by AutoCAD Civil 3D and Solidworks

## Slide 23: HPC: Urban Canyon Flow
Chart: Velocity (m/s)
| 4.528539999999996 | 5.6781299999999977 | 7.8095600000000003 | 9.3746434000000001 | 10.368849000000001 | 10.513579999999999 | 11.87503000000001 | 11.535489999999999 | 11.81256 | 12.35745 | 12.56579 | 11.895619999999999 | 11.4341872 | 10.4272072 | 10.344175399999999 | 10.310445 | 10.310525999999999 | 10.024486400000001 | 10.010985399999999 | 9.5372915999999996 | 9.5395336000000004 | 9.8704418000000071 | 10.132284 | 10.273201 | 10.132645999999999 | 9.6143749999999972 | 9.3412015999999998 | 9.2910436000000001
Boundary Layer with Surface roughness | 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.1 | 1.2 | 1.3 | 1.4 | 1.5 | 1.6 | 1.7 | 1.8 | 1.9 | 2 | 2.1 | 2.2 | 2.3 | 2.4 | 2.5 | 2.6 | 2.7
OpenFOAM used as the CFD program
Probes were placed in areas of interest to measure the important data

## Slide 24: HPC: Concept Car Comparison
The velocity plot could be used as an inlet for the concept car
It was then compared to a typical uniform inlet, giving a 30% increase in the drag force
Uniform 10m/s inlet
UDF
inlet

## Slide 25: HPC: The Ahmed Body
Simplified model of the geometry of a generic car
Used as a benchmark case for investigating automobile flow
CFD Online, 2005. File:Ahmed.gif. [online] Available at: http://www.cfd-online.com/Wiki/File:Ahmed.gif [Accessed 21/05/2014]

## Slide 26: HPC: Surrogate Modelling
Surrogate models are fast approximations of computationally expensive simulations based upon a limited set of data
Input Parameters
  Rear slant angle (5° - 45°)
  Fillet radius (0mm – 50mm)
Output Result
  Drag coefficient
Data set creation for surrogate model was automated & 35 simulations were run

## Slide 27: HPC: Surrogate Model Results
CFD Results Surrogate Model Results

## Slide 28: HPC: Turbulence
Turbulent flow causes flow properties to fluctuate irregularly about a mean value
Turbulence models are used to approximate small fluctuations seen in turbulent flow to reduce computational expense
Versteeg, H. K. and Malalasekera, W., 2007. An introduction to computational fluid dynamics: the finite volume method. 2nd ed. Harlow: Pearson Prentice Hall.
http://upload.wikimedia.org/wikipedia/commons/f/fb/Jet.jpg

## Slide 29: HPC: Turbulence Modelling Methods
3 common approaches:
  Reynolds-averaged Navier-Stokes (RANS)
    Fastest but ignores non-isotropic effects of eddies
  Large Eddy Simulation (LES)
    Directly resolves larger eddies – much more computationally demanding than RANS
  Hybrid Methods
    Combination of the two previous methods which can offer advantages to solution accuracy and computation time

## Slide 30: HPC: Turbulence Models Tested
Used Ahmed Body experimental results to validate turbulence models and numerical setups
RANS: k-ω SST, k-ε, RNG k-ε, Spalart-Allmaras
LES: One-Equation Eddy-Viscosity Model
  Unable to generate stable solutions
Hybrid: Delayed-Detached Eddy-Simulation
Lienhart, H., Stoots, C. and Becker, S., 2000. Flow and Turbulence Structures in the Wake of a Simplified Car Model (Ahmed Model)

## Slide 31: HPC: Vector Plots

## Slide 32: HPC: Drag Coefficients
Spalart-Allmaras Model | Rear Slant Angle | Experimental Drag Coefficient | Computed Drag Coefficient | Error %
 | 25° | 0.299 | 0.292 | -2.3%
 | 35° | 0.279 | 0.294 | 5.4%
Spalart-Allmaras model (RANS) gave most accurate drag results and flow topology
Did not correctly predict a drop in drag above the critical rear-slant angle
DDES results less accurate than Spalart-Allmaras
Correctly predicted a drop in drag above the critical rear-slant angle
DDES Model | Rear Slant Angle | Experimental Drag Coefficient | Computed Drag Coefficient | Error %
 | 25° | 0.299 | 0.341 | 14%
 | 35° | 0.279 | 0.294 | 5.4%

## Slide 33: HPC: Summary
Real-life flow profile shown to significantly affect the flow around the car model
Surrogate models may benefit the automotive industry by reducing the number of expensive CFD simulations needed
Spalart-Allmaras Turbulence Model generated the most accurate results
DDES correctly showed drop in drag seen beyond critical-slant angle

## Slide 34: Final Results: Concept Car

## Slide 35: Final Results: Testing

## Slide 36: Final Results: Drag Coefficient Comparison
 | Computational | Experimental
Straight Test | 0.167 | 0.17 ± 0.015
Angled Test | 0.298 | 0.358 ± 0.077

## Slide 37: Conclusions
Designed, manufactured and rendered a concept car
Successfully renovated existing wind tunnel to allow wake surveys and drag measurements
Created a Virtual Wind Tunnel (VWT) which accurately predicted the drag on an Ahmed body using RANS
Used the Ahmed body results to develop the VWT for the concept car
VWT drag results were compared with experimental results and were found to be in good agreement

## Slide 38: Any Questions?